## Slide 1
Utah Nanofab Design Review Meeting
Device Architecture (Top View Layout and Layer Cross Section)
Recipes & Settings
Standard
Concept
Equipment & Tools
Fabrication Processes
Custom
Researcher brings this to meeting
Nanofab Staff help determine this during meeting
DEPOSITION: ALD, PECVD, LPCVD, Sputter, E-beam
ETCH: XeF2, DRIE, RIE, Wet Etch, Laser Ablation
PHOTOLITHOGRAPHY: Spin Coat, UV Alignment
MEASURE: Thickness, Resistivity, Stress, Uniformity
PACKAGING: Dicing, Wire Bonding, Encapsulation
TIME POWER PRESSURE
FLOW TEMPERATURE FORCE
GASES CHEMICALS FREQUENCY
Concept
Architecture
Fabrication Processes
Equipment & Tools
Recipes & Settings

## Slide 2: Title of Research Project or Device To Be Fabricated
Researcher Name
PI Name
Date

## Slide 3: Abstract

## Slide 4: Design Concept
Goals:
Approach

## Slide 5: Applicable Graphs, Data, or Figures

## Slide 6: Device Architecture Top View and Cross Section Process Flow

## Slide 7: Proposed Materials and Fabrication Processes
Materials
    Substrate
    Thin films/coatings
    Chemicals
Processes
  Deposition
    Thin Films
    Coatings
  Patterning
    Photoresists
    Etching
  Packaging
    Dicing
    Wirebonding
Test and Measurement
    Electrical
    Mechanical
    Optical
    Fluidic

## Slide 8: References

## Slide 9: Example: Microfluidic Mixer
Brian Baker
Dr. Bruce Gale
July 4, 2016

## Slide 10: Example: Abstract
Mixing fluids over a wide range of flows inside microfluidic systems is challenging due to the laminar nature of fluids at the microscale. This study evaluates the design, fabrication, and testing of a passive three-dimensional micromixer that incorporates split and recombine structures that promote mixing at low flows with chaotic advection features that mix well at high flows. Comsol multi-physics simulations were performed to optimize the number of parallel channels, the channel width, and the number of split and recombine stages in the mixer. Overall mixer area was less than 4 mm2, and consisted of 19 stages of two parallel overlapping channels with a depth of 100 microns and a width of 50 microns. Soft lithography was used to fabricate the two-layer device, and during the assembly process a partial cure of PDMS was found to be especially useful for enabling successful alignment. Test results show mixing efficiencies above 92% across a range of flows from 0.1 mL/hr to 10 mL/hr, with a range of Reynold’s numbers from 0.28 to 28. At an intermediate flow rate of 1 mL/hr, a pressure drop of 1.7 kPa was measured, and the mixing speed was 98 milliseconds. Results show that combining two types of mixer structures in this manner can create high mixing efficiency with reduced overall mixer size.

## Slide 11: Example: Design Concept
Input 1
Input 2
Output
PDMS Layer 1
PDMS Layer 2
Goals:
  Increase mixing effectiveness/decrease time to mix at three flow rates
  Minimize pressure drop
  Minimize total area and length of mixer
  Simplify fabrication
  Build and test mixer based on simulation results
Approach
  Split and recombine multiple times results in many laminate layers
  Long, narrow channels increase diffusion
  Multiple parallel channels decrease pressure drop

## Slide 12: Example: Applicable Graphs, Data, or Figures

## Slide 13: Example: Device Architecture Top View and Cross Section Process Flow
Spin coat SU8
UV Expose and Develop
Mix and pour PDMS over mold, partial cure
Remove PDMS halves
Poke inlet holes in PDMS
Align and bond PDMS halves, fully cure
SU8
Silicon
PDMS

## Slide 14: Example: Proposed Materials and Fabrication Processes
Materials
  Substrate
    4” Silicon p-type wafer
  Thin films/coatings
    SU8 2050
  Chemicals
    Sylgard 184 PDMS
    SU8 Developer
Processes
  Deposition
    Coatings
      Sylgard 184 pour, vacuum degas and partial oven cure
  Patterning
    Photoresists
      SU8 spin and develop
      Align PDMS halves and fully cure
  Packaging
      Bore holes using coring tool
      Press fit fluidic tubes into inlet and outlet ports
  Test and Measurement
    Optical
      Microscope images of flows and mixing
    Fluidic
      Dual syringe pump with controlled flows and pressure gauge
      Colored water for enhanced mixing imaging

## Slide 15: Example: References
Squires, Todd M., and Stephen R. Quake. "Microfluidics: Fluid physics at the nanoliter scale." Reviews of modern physics 77.3 (2005): 977.
Nguyen, Nam-Trung, and Zhigang Wu. "Micromixers—a review." Journal of Micromechanics and Microengineering 15.2 (2005): R1.
Capretto, Lorenzo, et al. "Micromixing within microfluidic devices." Microfluidics. Springer Berlin Heidelberg, 2011. 27-68.
Chen, Hao, and Jens-Christian Meiners. "Topologic mixing on a microfluidic chip." Applied Physics Letters 84.12 (2004): 2193-2195.
SU8 Datasheet: http://microchem.com/pdf/SU-82000DataSheet2025thru2075Ver4.pdf, downloaded April 29, 2013.